## Slide 1: Improving Integration of Renewable Generation and Electric Vehicles
Peter A. O’Connor, Ph.D.
November 16, 2017

## Slide 2: Research Question
How do EVs and renewable energy fit together? Can EVs help the grid use more renewables?

## Slide 3: EVs on Current Grid

## Slide 4: The Potential of Smart Charging
100% EVs?
  ~3 Trillion VMT
  ~1000 TWh (25% increase)
Wind and solar
  Not dispatchable
  Rapid growth 2000-2016
Chart: Solar Installed (47 GW)
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Solar Installed | 4 | 11 | 23 | 45 | 58 | 79 | 105 | 160 | 298 | 382 | 851 | 1925 | 3372 | 4762 | 6251 | 7492 | 14626
Chart: Wind Installed (82 GW)
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Wind Installed | 71 | 1691 | 410 | 1665 | 397 | 2374 | 2457 | 5252 | 8363 | 10003 | 5215 | 6647 | 13082 | 1098 | 4767 | 8115 | 8191
Source: AWEA
Source: SEIA

## Slide 5: Vehicle-Grid Integration (VGI)
Reduce EVs’ own impact on the grid
Possibly help with other grid conditions

## Slide 6: Hourly Variability of Solar March 31, 2017
Chart: Megawatts
| 2.0833333333333405E-2 | 6.2500000000000111E-2 | 0.10416666666666716 | 0.14583333333333337 | 0.18750000000000031 | 0.22916666666666588 | 0.27083333333333293 | 0.31250000000000056 | 0.35416666666666674 | 0.39583333333333298 | 0.43750000000000056 | 0.47916666666666674 | 0.52083333333333304 | 0.5625 | 0.60416666666666596 | 0.64583333333333448 | 0.68750000000000067 | 0.72916666666666596 | 0.77083333333333393 | 0.8125 | 0.85416666666666596 | 0.89583333333333393 | 0.9375 | 0.97916666666666519
Total Load | 20678 | 20109 | 20070 | 19619 | 20016 | 21217 | 23388 | 24392 | 24052 | 23382 | 23488 | 23324 | 22802 | 22674 | 22743 | 22932 | 23589 | 23982 | 24439 | 25881 | 26215 | 25476 | 23796 | 22077
Net Load | 20675 | 20109 | 20070 | 19619 | 20016 | 21217 | 23362 | 22537 | 18916 | 16620 | 15640 | 15559 | 14600 | 14769 | 15090 | 15744 | 16919 | 19472 | 23098 | 25880 | 26215 | 25476 | 23796 | 22077

## Slide 7: Impacts of Increasing Solar
Non-dispatchable
Requires aligning supply and demand
  Hourly (load shifting) and minute-to-minute
  Ancillary services (e.g. regulation up/down)
Potential solutions compete on price
  Imports/exports
  Generator flexibility
  Stationary storage
  Demand flexibility (EVs, AC, water heaters)
Smart charging might not earn much revenue if high levels of PV are very easy to integrate

## Slide 8: Types of VGI
Basic “Smart Charging”
  Time of Use rates
Short-term ancillary services
  Demand response
  Frequency regulation
V2G
  Energy storage
  Concerns: Interconnection, Battery degradation
V2H or V2B
  Backup power when islanded

## Slide 9: Convening the Experts

## Slide 10: ~200 Attendees
Utilities
  Eversource, National Grid, Con Ed, Southern Company, Duke Energy, JEA, TVA, others
Car and Bus Manufacturers
  Ford, GM, BMW, Daimler, Nissan, Tesla, Deltawing
  BYD, Proterra, New Flyer
EV Charging Providers
  Networks, Installers, Manufacturers
Regulators, NGOs, Academics, Fleet Operators

## Slide 11: Modeling
Several studies in recent months (NREL, LBNL)
“Managed” vs “unmanaged” with ReEDS
  “Valley filling” but not more sophisticated capabilities
  Even rapid penetration only ~1.6% of generation in 2030
Reduced curtailment of RE and decreased CO2/kWh?
“Smart” > least-cost (unless include externalities)
  Account for generation and what is on the margin
  Changes are very minor and of uncertain confidence

## Slide 12: Findings
Technically feasible
Driver needs and preferences
Need value proposition
Local RE conditions vary
Data to utilities
Rate design
Stationary storage

## Slide 13: Pilot Projects
NRG & University of Delaware
  V2G
  Frequency Regulation (PJM)
Image from University of Delaware (http://www.udel.edu/udaily/2013/may/vehicles-grid-050213.html)

## Slide 14: Pilot Projects
EMotorWerks
  Smart Charging (one-way)
  Resource Adequacy
  Demand Response
  “Green Charging” option

## Slide 15: Pilot Projects
BMW/PG&E
  Smart Charging (one-way… sort of)
  Demand Response
  “Battery Second Life” as back-up
Image from BMW (http://content.bmwusa.com/bmwi_pge/index.html)

## Slide 16: Pilot Projects
Frito-Lay Trucks
  11 trucks (Smith Electric)
  Charge rate 10-11 kW, 3.5-5.5 hrs
Fast Responding Regulation Service (ERCOT)
  Full response within one second
  100 kW minimum threshold
Photo: Mike Simpson, NREL
http://www.nrel.gov/docs/fy14osti/61455.pdf

## Slide 17: Other Concepts
Off-grid PV-storage-solar chargers (Envision/Zam)
Microgrid systems (PowerTree, TimberRock, SDG&E)

## Slide 18: Obstacle: Rules and Standards
Rules for market participation
  Minimum resource size
  Telemetry requirements
  Interconnection
Competing standards
  Rooted in trust/control concerns?
  Hardware is natively interoperable

## Slide 19: Obstacle: Technical Issues
Technology integration (case-by-case basis)
V2G Battery life impacts
  Revenue exceeds marginal cost, or don’t bid in
    At $200/kWh and 1000 cycle life, $0.20/kWh breakeven
    Pilot projects can tolerate lower value
    Third-party aggregators would ideally disclose calculations and let EV owners modify bid price
  Research continues on relative impacts of V2G compared to driving
  Not an issue for one-way smart charging

## Slide 20: Obstacle: Value Proposition
TOU?
  Easy, but misses daily variations
Day-ahead dynamic pricing?
  SDG&E pilot
DR and ancillary services are technically proven, but:
  Can’t extrapolate value from PJM regulation market
  Cost of additional communication layer uncertain
  TOU leads to “pre-emptive DR”
More EVs make it easier to predict availability
Most important issue: the use case
What do you want to accomplish?

## Slide 21: What is the Value?
If grid integration is easy, don’t even need smart charging
If grid integration is hard, will have high value for both smart charging and storage
Value shows up in ancillary services prices
Options will compete
Know what service you are providing

## Slide 22: When Will We Need Storage for VER?
Integration cost estimates generally low
  Milligan et al. 2011, Mills et al. 2013, Cohen et al. 2015
Actual experience: easier than expected
  Storage needed at 70-80% of energy from VER?
Models of high-RE California future show the state could deploy less storage and more flexible loads to accommodate RE at lower cost

## Slide 23: Recommendations
Workplace Charging
Time-Varying Rates
Distribution Benefits
Ancillary Services
Storage Procurements/Policies and V2G
Define “Smart”
Pilot Projects
ucsusa.org/smartcharging

## Slide 24: Grid Modernization

## Slide 25: Game-Changers
Cheap stationary storage
  Unlikely to entirely remove value of “smart charging”
  Ancillary market access useful for both flexible loads and storage
  Impacts business case for “battery second life”
    How much retained value vs. new batteries?
Shared autonomous vehicles
  Possibly far fewer vehicles on the road
  Would want to charge as fast as possible
  Home “smart chargers” as stranded assets
Dynamic wireless charging?